## Slide 1: Chapter 3
Rate Laws and Stoichiometry

## Slide 2: Overview
In chapter 2, we learned we can calculate volume to achieve a specified X if we have
In this chapter we’ll learn how to find this function by two steps
  Relate reaction rate vs concentrations
  Relate the concentrations vs the conversion

## Slide 3: 3.1 Basic Definitions
Homogeneous reaction
  involves only one phase
Heterogeneous reaction
  involves more than one phase
Irreversible reactioin
  proceeds in one direction
  Continues until the reactants are consumed
  When quilibrium point lies close to the product side
Reversible reaction
  can proceed in either direction depending on the reactants and products conc. relative to the corresponding equilibrium conc
Molecularity reaction
  The number of atoms or molucules involved in the reaction
  Unimolecular, bimolecular and termolecular

## Slide 5: 3.2 The reaction order and rate law
Rate law is the algebraic expression that relates –rA to the species concentrations
3.2.1 Power law models for elementary rate laws
In the power law, the rate law is the product of concentartions of the indivisual reacting specise raised to a power
Reaction order is the powers to which the concs are raised to
α=order w.r.t. A β= order w.r.t B overall order(n)= α+ β kA=reaction rate constant, has the unit of (conc)1-n/time
For the reaction A→P
Reaction order, n | Rate law | k
zero |  | mol/dm3.s
1st |  | s-1
2nd |  | dm3/mol.s

## Slide 6
Elemntary reaction
  Involves a single step
  Stoichiometric coefficients are identical to the powers in the rate law
  Many non elementary teaction follow an elementary rate law (Stoichiometric coefficients are identical to the powers in the rate law)
Rate laws are Experminentally dtermeined

## Slide 8: Reversible Reactions
Consider the rev. reaction
Equilibrium constant KC is defined as
The net reaction rate is the sum of the forward and backward reactions
At Equilibrium the net reaction rate for all species is zero

## Slide 9: 3.3 Reaction rate constant
In most laboratory and industrial reactions it is assumed that Ka depends only on temperature
Arrhenius Equation
A=pre-exponential or frequency factor, E activation energy J/mol, R=gas constant, T=absolute temperature
Activation energy is related to the energy barrier that the reactants must overcome to react

## Slide 10
Taking logarithm of Arrhenius equation yields
E can be determined experimentally by carrying out the reaction at several different temperatures
If we know k(T0) we can find k(T)by